## Slide 1
EarthCARE ESA Data Products
Tobias Wehr
tobias.wehr@esa.int
16/02/2022

## Slide 2
EarthCARE
Observations:
Cloud profiles (ice, liquid, mixed), cloud coverage, precipitation
Aerosol profiles
Broad-band Solar & Thermal Radiation
Satellite and Payload
Sun-sync. orbit at 393 km, 14:00 hours descending node
UV Lidar with high spectral resolution receiver
W-band Cloud Radar with Doppler (contribution JAXA)
Imager and Broad-Band Radiometer
Launch October 2023
CPR – Cloud Profiling Radar W-Band with Doppler
ATLID – Atmospheric Lidar 355 nm HSRL with depol. channel
MSI – Multi-Spectral Imager 4 solar, 3 thermal channels
BBR – Broad-Band Radiometer 3 FoV (forward, nadir, backwards), broadband solar and thermal channel
Notes: high confidence that system integration can be completed this summer, then system testing at ESTEC for about a year, then launch campaign. high confidence Oct 2023 launch. Hopefully, EarthCARE will come to ESTEC in June.

## Slide 3
3
ESA L2b
ESA L2a
Nomenclature of data products
YYY-ZZZ YYY: instrument IDs, ZZZ: content reference
Examples:
A-FM ATLID-derived Feature Mask
AM-CTH ATLID & MSI-derived Cloud Top Height
Exception: supporting products X-MET & X-JSG

## Slide 4
4
EarthCARE Data Product Tree
ESA data products will be produced operationally by the ESA ground segment located at ESRIN.
JAXA data products fall in two categories:
Standard Products: produced and released by JAXA Mission Operation System:
(1) CPR echo and cloud products; (2) ATLID feature & target mask, aerosol & cloud products, PBL height; (3) MSI cloud products; (4) CPR-ATLID synergistic cloud products; (5) CPR-ATLID-MSI synergistic cloud products; (6) Four-sensor synergy radiative products.
Research Products: processed by either JAXA/EORC or co-operating Japanese Laboratories, are single or multi-sensor cloud, aerosol, precipitation, snow and air motion products.
L0 and L1 calibration products not distributed to regular users
ESA L2b
ESA L2a
geophysical retrievals per instrument
 14 products
ESA L2a
synergistic retrievals
 11 products
ESA L2b

## Slide 5
5
EarthCARE Data Product Tree
ESA data products will be produced operationally by the ESA ground segment located at ESRIN.
JAXA data products fall in two categories:
Standard Products: produced and released by JAXA Mission Operation System:
(1) CPR echo and cloud products; (2) ATLID feature & target mask, aerosol & cloud products, PBL height; (3) MSI cloud products; (4) CPR-ATLID synergistic cloud products; (5) CPR-ATLID-MSI synergistic cloud products; (6) Four-sensor synergy radiative products.
Research Products: processed by either JAXA/EORC or co-operating Japanese Laboratories, are single or multi-sensor cloud, aerosol, precipitation, snow and air motion products.
L0 and L1 calibration products not distributed to regular users
ESA L2b
ESA L2a
X-MET:
meteorological forecast data collocated with EarthCARE swath
used for data product generation
provided by ECMWF
X-JSG: Joint Standard Grid
used as retrieval grid for many L2 data products
Definition:
vertical, following lidar: approx. 103 m
along-track, following radar*: approx. 1 km *2 radar pixels
across-track resolution: fixed 1 km
X-MET and X-JSG Products

## Slide 6
6
EarthCARE Data Product Tree
ESA data products will be produced operationally by the ESA ground segment located at ESRIN.
JAXA data products fall in two categories:
Standard Products: produced and released by JAXA Mission Operation System:
(1) CPR echo and cloud products; (2) ATLID feature & target mask, aerosol & cloud products, PBL height; (3) MSI cloud products; (4) CPR-ATLID synergistic cloud products; (5) CPR-ATLID-MSI synergistic cloud products; (6) Four-sensor synergy radiative products.
Research Products: processed by either JAXA/EORC or co-operating Japanese Laboratories, are single or multi-sensor cloud, aerosol, precipitation, snow and air motion products.
L0 and L1 calibration products not distributed to regular users
ESA L2b
ESA L2a
C-NOM:
radar reflectivity (dBZ)
Doppler velocity (m/s)
A-NOM:
attenuated backscatter in
“Mie” channel, “Rayleigh” channel, cross-polar channel
M-NOM:
radiances in solar channels
TB in thermal channels
M-RGR:
radiances in solar channels, re-gridded
TB in thermal channels, re-gridded
Since the seven channels of MSI are not accurately aligned, this product uses one (selectable) channel as reference and spatially re-samples all other channels to the reference channels, so that all channels are fully aligned.
(Note: on the MSI own grid, not on the JSG.)
B-NOM:
Filtered SW and LW radiances
resolutions: 10km x 10km (standard)
5km x 10km (small)
17/28km x 10km (full)
B-SNG:
Filtered SW and LW radiances
high resolution corresponding to along-track sampling and detector resolution  usage: customise spatial resolution
Note: These data products contain filtered radiances, which are scientifically not directly useable, before unfiltering has happened. Therefore: science users advised to use BM-RAD product!
Level 1 Products

## Slide 7
Synergistic Level 2b
1. Target classification
2. Cloud & aer. prof. at x-sec
ATLID Level 1b (ESA)
Attenuated backscatter in
Rayleigh channel
Co-polar Mie channel
Cross-polar Mie channel
CPR Level 1b (JAXA)
Radar reflectivity and Doppler velocity profiles
MSI Level 1b/c (ESA)
TOA radiances for four solar channels, TOA brightness temperatures for three thermal channels
ATLID Level 2a
Feature mask and target classification, extinction, backscatter & depol. profiles, aerosol properties, ice cloud properties, ...
CPR Level 2a
Radar echo product, feature mask, cloud type, liquid and ice cloud properties, vertical motion, rain and snow estimates, ...
MSI Level 2a
Cloud mask, cloud micro-physical parameters, cloud top height, aerosol parameters, ...
EarthCARE Data Production Model

## Slide 8
MSI Level 1b/c (ESA)
TOA radiances for four solar channels, TOA brightness temperatures for three thermal channels
MSI Level 2a
Cloud mask, cloud micro-physical parameters, cloud top height, aerosol parameters, ...
EarthCARE Data Production Model
Synergistic Level 2b
1. Target classification
2. Cloud & aer. prof. at x-sec
ATLID Level 1b (ESA)
Attenuated backscatter in
Rayleigh channel
Co-polar Mie channel
Cross-polar Mie channel
CPR Level 1b (JAXA)
Radar reflectivity and Doppler velocity profiles
ATLID Level 2a
Feature mask and target classification, extinction, backscatter & depol. profiles, aerosol properties, ice cloud properties, ...
CPR Level 2a
Radar echo product, feature mask, cloud type, liquid and ice cloud properties, vertical motion, rain and snow estimates, ...
synergistic target classification
CAPTIVATE Algorithm
Synergistic Retrievals
acknowledgements: KNMI, LATMOS, ECMWF
Notes: ATLID Level 1 is noisy, difficult to detect weak features – it is not recommended to use a threshold-based detection of features, instead, use A-FM (image processing methods to identify features)

## Slide 9
Synergistic Level 2b
1. Target classification
2. Cloud & aer. prof. at x-sec
ATLID Level 1b (ESA)
Attenuated backscatter in
Rayleigh channel
Co-polar Mie channel
Cross-polar Mie channel
CPR Level 1b (JAXA)
Radar reflectivity and Doppler velocity profiles
MSI Level 1b/c (ESA)
TOA radiances for four solar channels, TOA brightness temperatures for three thermal channels
ATLID Level 2a
Feature mask and target classification, extinction, backscatter & depol. profiles, aerosol properties, ice cloud properties, ...
CPR Level 2a
Radar echo product, feature mask, cloud type, liquid and ice cloud properties, vertical motion, rain and snow estimates, ...
MSI Level 2a
Cloud mask, cloud micro-physical parameters, cloud top height, aerosol parameters, ...
3D Scenes Construction
Expand syn. retrievals across-track using MSI; ≈40km wide
EarthCARE Data Production Model
Radiative Transfer Products
calculated radiances, fluxes, heating rate profiles
acknowledgements: Environment and Climate Change Canada
Notes: Radiative transfer on three-dimensional scenes of cloud/aerosol/precip information retrieved from ATLID, CPR, MSI  calculate radiances, fluxes, heating rates (ACM-RT product). TOA radiances and flux are then compared to BBR observations (BM-RAD, BMA-FLX). The result of the comparison is reported in the ACMB-DF product (in terms of probability functions). Note, ACM-RT does not make any use of BBR information, therefore, the comparison to BM-RAD and BMA-FLX is independent. The purpose of this is to evaluate the quality of the cloud/aerosol/precip retrievals against the BBR measurements.

## Slide 10
Synergistic Level 2b
1. Target classification
2. Cloud & aer. prof. at x-sec
ATLID Level 1b (ESA)
Attenuated backscatter in
Rayleigh channel
Co-polar Mie channel
Cross-polar Mie channel
CPR Level 1b (JAXA)
Radar reflectivity and Doppler velocity profiles
MSI Level 1b/c (ESA)
TOA radiances for four solar channels, TOA brightness temperatures for three thermal channels
BBR Level 1b (ESA)
Filtered TOA short-wave and total-wave radiances
ATLID Level 2a
Feature mask and target classification, extinction, backscatter & depol. profiles, aerosol properties, ice cloud properties, ...
CPR Level 2a
Radar echo product, feature mask, cloud type, liquid and ice cloud properties, vertical motion, rain and snow estimates, ...
MSI Level 2a
Cloud mask, cloud micro-physical parameters, cloud top height, aerosol parameters, ...
BBR Level 2a
Unfiltered top-of-atmosphere radiances, short-wave and long-wave fluxes
BBR Level 2b: enhanced products using MSI
Assessment
Comparison of calculated fluxes and radiances to BBR observations
3D Scenes Construction
Expand syn. retrievals across-track using MSI; ≈40km wide
Radiative Transfer Products
calculated radiances, fluxes, heating rate profiles
EarthCARE Data Production Model
Slide 10

## Slide 11
11
Test Scene
(“Halifax”)
Reconstructed cloud scene
based on radar-only + lidar-only + imager-only cloud retrievals
(“Composite” product)
FLUX IN BLUE
Synergistically retrieved
cloud scene, CAPTIVATE
algorithm (Opt. Estimation with complex state vector)
FLUX IN YELLOW
Model truth (Canadian
Weather Model GEM)
FLUX IN RED
Acknowledgement
R. Hogan, S. Mason, H. Barker, Y. Cole, Z. Qu, D. Donovan
Retrievals and “Closure”
Example of work in progress
 “Composite” clouds are too dull and too cold

## Slide 12
“Halifax” scene “Baja” scene “Hawaii” scene
Algorithm testing
Three high-resolution scenes from the Canadian GEM model have been generated
Level 2 Algorithm Theoretical Basis Descriptions to be published in Atmospheric Measurement Techniques Special Issue on “EarthCARE Level 2 algorithms and data products”  paper submission target is June 2022
Test Data are available for the three test scenes
Level 2 products produced by European/Canadian team (based on simulated Level 1 data produced by science team)
Level 1 data produced by ESA processors
A-NOM, M-NOM, M-RGR, B-NOM, B-SNG
(some issues to be resolved, not yet chained with Level 2 processors in production model)
Data available on ftp account – request access from ESA
However, recommended to wait for a few months until Level 1–Level 2 chain completed!

## Slide 13
  Level 2 Team
  ATLID retrievals G.-J. van Zadelhoff, D. Donovan(KNMI, Netherlands)
  CPR products P. Kollias, B. Puigdomenech (McGill University, Canada); A. Battaglia (University of Torino, Italy)
  MSI retrievals A. Hünerbein, S. Bley (TROPOS, Germany); N. Docter, R. Preusker, J. Fischer (Free University of Berlin, Germany)
  BBR radiances and estimated fluxes N. Clerbaux, A. Velazquez, E. Baudrez (Royal Meteorological Institute Belgium); C. Domenech, R. Garcia Maranon (GMV Madrid), J. Fischer (Free University of Berlin, Germany)
  Synergistic ATLID & MSI retrievals U. Wandinger, A. Hünerbein, M. Haarig (TROPOS, Germany)
  Synergistic CPR & ATLID & MSI retrievals R. Hogan, S. Mason (ECMWF, UK); J. Delanoë, A. Irbah (LATMOS, France)
  Radiation products (from retrievals) & closure H. Barker, J. Cole, M. Shephard, Z. Qu (Environment and Climate Change Canada); N. Villefranque (LMD/IPSL, France)
  ECMWF Assimilation
  M. Janiskova, M. Fielding
Acknowledgments
The EarthCARE Joint Mission Advisory Group
Co-chairs: A.J. Illingworth, H. Okamoto
Members: L. Baldini, A. Battaglia, H. Chepfer, N. Clerbaux, J. Cole, J. Delanoë, D. Donovan, J. Fischer, S. Groß, R. Hogan, T.Y. Nakajima, T. Nishizawa, Y. Ohno, M. Satoh, K. Suzuki, N. Takahashi, U. Wandinger
Observers: S. Kato, G. Stephens, B. Stevens, D. Vane, D. Winker
A. J. Illingworth et al.
The EarthCARE satellite: The next step forward in global measurements of clouds, aerosols, precipitation and radiation
http://journals.ametsoc.org/doi/pdf/10.1175/BAMS-D-12-00227.1